On the Descent of Programs from Reconfigurable Hardware
LambdaConf 2016
(20160528T193000Z)
Jimmy Torre
jpt4 - torreaiworks01@gmail.com – B513A513 - KC9YYY

---
Pervasively Reconfigurable Computing (PRC)
www.github.com/jpt4/prc

---
Telos
Collapse the abstraction stack between physical and logical semantics.
Architecture A => A-asm => miniFORTH => miniLISP => Shen => ShenOS ...
!!!~~~~>INTEL<~~~~!!!
Architecture B => B-asm => ...
Hardware Circuits => Control Signals => Microcode => Internal ASM => ...

---
Thesis
A Universal Cell (UC) is a
:reversible (parity conserving)
:asynchronous
:reprogrammable (partial, dynamic)
automaton capable of supporting
:binary switching logic
:memory
:signal routing
as a unified, primitive circuit element.
Mem = L/1
Mem = R/0
A
A'
B'
C
C'
B
A'
B
C
C'
B'
A

---
Ethos I
Reversible Logic
:bijective mapping
:k*T*ln(B)
:Fredkin Gate
A B C A’B’C’
0 0 0 <-> 0 0 0
0 0 1 <-> 0 0 1
0 1 0 <-> 0 1 0
0 1 1 <-> 0 1 1
1 0 0 <-> 1 0 0
1 0 1 <-> 1 1 0
1 1 0 <-> 1 0 1
1 1 1 <-> 1 1 1
Asynchronous Logic
:no clock
:local data flow control
:Muller C-Gate
A B Cn
0 0 -> 0
0 1 -> C(n-1)
1 0 -> C(n-1)
1 1 -> 1

---
Ethos II
Reconfigurable Logic
:FPG/TA, PLA
:logic slice/interconnect network
:spintronic, magnetoresistive gates
Transistor
:”close to the physics”
:general purpose
:single-transistor NOR gate

---
Logos I
Reconfigurable Asynchronous Logic Automata
:uniform grid
:token passing
:stem vs. gate cells
Reversible Logic Elements with Memory
:combined switching, memory operations
:naturally geometric
:RLEM 3-453
A
A'
A
A'
B
B'
B
B'
C
C'
C
C'
“L/1”
3-453
“R/0”

---
Logos II
Geometrically Explicit Logic Circuits
:a regular array of “triangular” RLEMs is Turing Complete
RLEM 2-3/4 via RLEM 3-453
Build Order:
1. C’(3) -> C(3)
2. A’(3) -> B(2)
3. C’(1) -> B(3)
4. A’(1) -> A(2)
5. B’(3) -> C(2)
6. B’(1) -> A(3)
7. A’(2) -> C(1)
8. S ->
9. T ->
10. -> A
11. -> B
GELC for RLEM 2-3/4 via triangular RLEM 3-453
A
B
1
2
3
2
S
T
1
L6
L5
L5
L5
L5
R1
R1
L6
R7
R7
R7
R7
L6
L5
L5
R7
R7
R7
R7
L5
R7
R7
R7
L7
R7
R7
R4
L10
B
T
L9
R4
2
L5
R8
S
L5
L5
A
R5
L5
L6
R7
R7
R7
R7
L6
L5
R1
R1
R1
3
R2
L2

---
Logos III
Universal Cells
:stem, processor (proc) and wire roles
:binary logic plus null (0, 1, _)
:pull-based asynchronous data flow
:special messages and standard signals
[role, mem, high-rail, buffer, self-mailbox, input, output]
Special Messages
:Target
00 -> Self
01 -> A neighbor
10 -> B neighbor
11 -> C neighbor
:Command
000 -> become stem
001 -> become wire left
010 -> become wire right
011 -> become proc left
100 -> become proc right
101 -> standard signal 1
110 -> standard signal 0
111 -> undefined
Pull-based data flow
:multi-stream
:collect all neighbors’ output
:self output blocks collection
A'
C
B
A
C'
B'
B'
C'
A
B
C
A'
C
A'
B
C'
B'
A
A
B'
C'
B
A'
C
A'
C
B
A
C'
B'
B'
C'
A
B
C
A'

---
Logos IV
Switchable Latching Ferrite EMF Circulators
:geometric waveguide
:3 (triangular) or 4 (rectangular) channel
:magnetic remanence refractory period limits throughput
:1960s tech

---
Pathos
Totemic Computing
:peer computer
:explicit external incarnation of skill
:self-hosted Bene Gesserit artificial intelligence

---
Anabasis
:Rule formalization, minimization
:Externally evident stem state?
:Automatic circuit synthesis
:Quasi-delay independent UC functions
:UC matrix visualization
:Alternative physical implementation

---
Epilogue
[0] Magnetic-field-controlled reconfigurable semiconductor logic. Joo, S., et al.
    http://www.ncbi.nlm.nih.gov/pubmed/23364687
[1] Transistor NOR Gate.
    http://hyperphysics.phy- astr.gsu.edu/Hbase/Electronic/trangate.html#c5
[2] Reconfigurable Asynchronous Logic Automata (RALA).
    Gershenfeld, N., Dalrymple, D. http://cba.mit.edu/docs/papers/09.11.POPL.pdf
[3] Reversible Logic Elements with Memory and
    Their Universality. Morita, K. http://arxiv.org/pdf/1309.1264v1.pdf
[4] Quasi-delay insensitive circuits are Turing-complete.
    Manohar, R. and Martin, A. http://vlsi.cornell.edu/~rajit/ps/qdi.pdf
[5] A New Type of Latching Switchable Ferrite Junction Circulator. Siekanowicz, W. and Schilling, W.
    http://www.ecs.umass.edu/ece/sdp/sdp06/siqueira/ papers/01126638.pdf